## Slide 1: Batteryless Hydrometer
Lightning Talk 3: Technical Challenges
Group Members: Tilden Chen, Josh Hall, Jensen Mayes, Chris McGrory, Griffin Orr, Chris Pedersen
Client: Henry Duwe

## Slide 2: Challenge: Physical Encapsulation
Learning a 3D modeling tool: SolidWorks
Relating the density physics to the accelerometer output
Creating a testing model
Creating a testing environment
Balancing the onboard electronics

## Slide 3: Challenge: Orientation Detection
ICM-20648
  6-Axis Inertial Sensor
    3-axis gyroscope
    3-axis accelerometer
Testing
  Encapsulated design
    Adding salt to bucket of water
    Calibrating output to measure specific gravity

## Slide 4: Challenge: Tilt Mechanics
Challenging to calculate the system response due to several factors:
  Difficult to calculate weight distribution
  Each prototype will be slightly different
  The center of buoyancy changes due to the change in density to cause the change in tilt
Determine torque created by the system to align the center of mass and the center of buoyancy
Testing the system will involve:
  Using a simplified model to prove feasibility mathematically
  Building a prototype with similar mass distribution to the simplified model
  Testing the prototype by increasing density of a sample tank

## Slide 5: Challenge: Hardware Development
No lab access
  Minimal ability to assemble PCBs
  No access to reflow oven
  Limited access to ETG
RF Development
  Limited access to on-campus resources such as network analyzer
  Limited access to faculty

## Slide 6: Challenge: Software
Raspberry Pi Software
  We have been having issues getting and mapping the correct Bluetooth beacon libraries to be able to receive Bluetooth beacons from any sending device
MCU Software
  We foresee the biggest difficulty on the software side being with writing the code for the MCU.
  Will need to make the code efficient enough to gather the sensor data and send the information over Bluetooth (preferably a few times before losing power).

## Slide 7: Challenge: Testing
No equipment access
Alternative Methods of Testing
  Postpone testing
  Simple Tests individual team members can do from home
  Software